Name: _________ANSWER KEY _____________ Date: __________________________ Period: _______

Calculations with Thermal Energy and Heat

Q = mc∆T, where Q = heat energy, m = mass, and ∆T = change in temp.

Remember, ∆T = (Tfinal – Tinitial).  Show all work and proper units.

- A 0.01575 kg piece of iron absorbs 1086.75 joules of heat energy, and its temperature changes from 25 K to 175 K.  Calculate the specific heat capacity of iron.

C =        Q        =       1086.75         =  460 J/kgK

m(Tf-Ti)        0.01575(175-25)

- How many joules of heat are needed to raise the temperature of 0.01 kg of aluminum from 22 K to 55 K, if the specific heat of aluminum is 900 J/kgK?

Q = mC(Tf – Ti) = 0.01 kg (900J/g°C)(55-22) = 297 J

- Calculate the specific heat capacity of a piece of wood if 1.5 kg of the wood absorbs 67,500 joules of heat, and its temperature changes from 32 K to 57 K.

C =        Q        =         67500 J       =     1800 J/kgK

m(Tf-Ti)	   (1.5 kg)(57-32)

- 0.1 kg of 204 K water is heated until its temperature is 237 K.  Calculate the amount of heat energy needed to cause this rise in temperature.

Q = mC(Tf-Ti) = 0.01 kg(4184J/kgK)(237 – 204) = 13807 J

- 0.025 kg of mercury is heated from 125 K to 255 K, and absorbs 455 joules of heat in the process.  Calculate the specific heat capacity of mercury.

C =       Q       =         455 J             =   140 J/kgK

m(Tf-Ti)      (0.025g)(255-125)

- What is the specific heat capacity of silver metal if 0.055 kg of the metal absorbs 47.3J of heat and the temperature rises 15.0 K?

C =     Q     =  	    47.3 J         =    57.3 J/kgK

m(Tf-Ti)      (0.055 kg)(15)

- What mass of water will change its temperature by 3 K when 525 J of heat is added to it?

m =       Q       =             525 J            =  0.0418 kg

C(Tf–Ti)        (4184J/kgK)(3)

- A 0.0003 g piece of copper is heated and fashioned into a bracelet.  The amount of energy transferred by heat to the copper is 66.3 J.  If the specific heat of copper is 390 J/kgK, what is the change of the copper's temperature?

ΔT =   Q     =       66.3 J           = 567 K

mC         0.0003kg(390J/kgK)

# Text boxes

Q

ΔT

c

m